## Slide 1
Al-Azhar University
Faculty of Engineering
Systems and Computer Engineering Dept.
Intelligent Systems Engineering Program
Prof. Ahmed Youssef
ENG 142
Digital and Logic Design (2)

## Slide 2: Course Contents
1 | Introduction | W1
2 | Sequential Logic Circuits | W2 - W3
3 | Sequential Logic Circuits Analysis | W4 - W5
4 | Sequential Logic Circuits Design | W6 - W7
5 | Registers, Counters | W9 – W11
6 | Programmable Devices | W12
7 | VHDL Circuit Simulation | W13

## Slide 4
Grading Policy
100
40
Final Exam
30
30 Practical
Notes: 4

## Slide 5: Logic Gates

## Slide 6: Combinational Circuits
  n input bits  2n possible binary input combinations
  Examples: adders, subtractors, comparators, decoders, encoders, and multiplexers.
Combinational
circuit
(logic gates)
n binary
inputs
m binary
outputs

## Slide 7: Full Adder Using Half Adders
x
y
C
S
z
HA
HA

## Slide 8: Integer Addition 2/2
FA
x
y
z
C
S
a0
b0
C0=0
S0
C1
FA
x
y
z
C
S
a1
b1
S1
C2
FA
x
y
z
C
S
a2
b2
S2
C3
FA
x
y
z
C
S
a3
b3
S3
C4
Ripple-carry adder

## Slide 9: Decoders
In general, for an n-bit code, a decoder could select up to 2n lines:
:
:
n-bit
code
n to 2n
decoder
2n
output lines

## Slide 10: Decoder Example
2-to-4-Line Decoder
A
1
0
0
1
1
A
0
0
1
0
1
D
0
1
0
0
0
D
1
0
1
0
0
D
2
0
0
1
0
D
3
0
0
0
1
(a)
D
0
5
A
1
A
0
D
1
5
A
1
A
0
D
2
5
A
1
A
0
D
3
5
A
1
A
0
(b)
A
1
A
0

## Slide 11: 4-to-1-Line Multiplexer: Circuit
S0
I0
Y
I1
I2
I3
S1
I0
I1
MUX
Y
S1
0
1
I2
I3
2
3
S0
Y = S1’S0’I0 + S1’S0I1 + S1S0’I2 + S1S0I3

## Slide 12: Digital Design
With an Introduction to the Verilog HDL, VHDL, and SystemVerilog 6th Edition
Chapter 05
Synchronous Sequential Logic

## Slide 13: Sequential Circuits Model
Combinational
Circuit
inputs
outputs
Memory
Elements
current
state
next
state
current state is a function of past inputs and initial state

## Slide 14: Classification
Two types of sequential circuits
Synchronous
  The state of the memory elements are updated with the arrival of each pulse
  Synchronization is usually achieved through the use of a common clock
Asynchronous
  No clock
  behavior of an asynchronous sequential circuits depends upon the input signals at any instant of time and the order in which the inputs change.

## Slide 15: Clocked Sequential Circuits
Memory elements are flip-flops which are logic devices, each of which is capable of storing one bit of information.
Combinational
Circuit
Flip-Flops
inputs
outputs
current
state
next
state
clock

## Slide 16: Clocked Sequential Circuits
The outputs of a clocked sequential circuit can come from the combinational circuit, from the outputs of the flip-flops or both.
The state of the flip-flops can change only during a clock pulse transition
  i.e. low-to-high and high-to-low
  clock edge
When the clock maintains its value, the flip-flop output does not change
The transition from one state to the next occurs at the clock edge.

## Slide 17: Latches
The most basic types of memory elements are latches.
A latch is a memory device that can maintain a binary state.
Latches are, in fact, asynchronous devices and they usually do not require a clock to operate.

## Slide 18: NAND/NOR
NAND
Any I/P =0  O/P = 1
All I/Ps =1  O/P = 0
NOR
Any I/P =1  O/P = 0
All I/Ps =0 O/P = 1

## Slide 19: SR-Latch
made of cross-coupled NOR (or NAND) gates
R
Q
S
Q’
R | S | Q(t) | Q(t+1) | State
0 | 0 | 0 |  | 
0 | 0 | 1 |  | 
0 | 1 | 0 |  | 
0 | 1 | 1 |  | 
1 | 0 | 0 |  | 
1 | 0 | 1 |  | 
1 | 1 | 0 |  | 
1 | 1 | 1 |  | 

## Slide 20: SR-Latch
made of cross-coupled NOR (or NAND) gates
R
Q
S
Q’
R | S | Q(t) | Q(t+1) | State
0 | 0 | 0 | 0 | No Change
0 | 0 | 1 | 1 | No Change
0 | 1 | 0 | 1 | Set
0 | 1 | 1 | 1 | Set
1 | 0 | 0 | 0 | Reset
1 | 0 | 1 | 0 | Reset
1 | 1 | 0 | ? | Undefined
1 | 1 | 1 | ? | Undefined

## Slide 21: SR-Latches with NAND Gates
S
Q
R
Q’
Also known as S’R’-latch
R | S | Q(t) | Q(t+1) | State
0 | 0 | 0 | ? | Undefined
0 | 0 | 1 | ? | Undefined
0 | 1 | 0 | 0 | Reset
0 | 1 | 1 | 0 | Reset
1 | 0 | 0 | 1 | Set
1 | 0 | 1 | 1 | Set
1 | 1 | 0 | 0 | No Change
1 | 1 | 1 | 1 | No Change

## Slide 22: SR-Latch with Control Input
Control inputs allow the changes at S and R to change the state of the latch.
Q
Q’
R
S
C
C | S | R | Q | Q’
0 | X | X | No change | 
1 | 0 | 0 | No change | 
1 | 0 | 1 | Q = 0 | Reset state
1 | 1 | 0 | Q = 1 | Set state
1 | 1 | 1 | Indeterminate | 

## Slide 23: D-Latch
SR latches are seldom used in practice because the indeterminate state may cause instability
Remedy: D-latches
R
Q
S
Q’
This circuit guarantees that the inputs to the S’R’-latch
is always complement of each other when C = 1.
C
D

## Slide 24: D-Latch as a Storage Unit
D–latches can be used as temporary storage
The input of D-latch is transferred to the Q output when C = 1
When C = 0 the binary information is retained.

## Slide 25: Graphic symbols for latches.

## Slide 26: Need for Flip-Flops
Outputs may keep changing so long as C = 1
Combinational
Circuit
Latches
inputs
outputs
current
state
next
state
C

## Slide 27: Need for Flip-Flops
  The states of the memory elements must change synchronously
  memory elements should respond to the changes in input at certain points in time.
  This is the very characteristics of synchronous circuits.
  To this end, we use flip-flops that change states during a signal transition of control input (clock)

## Slide 28: Clock response in flip-flop.

## Slide 29: Edge-Triggered D Flip-Flop
An edge-triggered D flip-flop can be constructed using two D latches
D latch
(master)
D
C
Q
D latch
(slave)
D
C
Q
clk
D
Q
Y
clk’
Q = Y = D
Y = D
clk
Y does not change
Negative edge-triggered
D flip-flop
clk’
clk
D
Y
Q

## Slide 30: Positive Edge-Triggered D Flip-Flop
D latch
(master)
D
C
Q
D latch
(slave)
D
C
Q
D
clk
Q
Y
clk
clk’
Y= D
clk’
Y does not change
clk
Q = Y = D

## Slide 31: Symbols for D Flip-Flops
D FF
D
Q
clk
C
Positive edge-triggered
D Flip-Flop
D FF
D
Q
clk
C
Negative edge-triggered
D Flip-Flop

## Slide 32: D Flip-Flop
Characteristic equation
  Q(t+1) = D
D FF
D
Q
clk
C
Positive edge-triggered
D Flip-Flop
D | Q(t+1)
0 | 0
1 | 1
Characteristic Table

## Slide 33: Other Flip-Flops
D flip-flop is the most common
  since it requires the fewest number of gates to construct.
Two other widely used flip-flops
  JK flip-flops
  T flip-flops
JK flip-flops
  Three FF operations
    Set
    Reset
    Complement

## Slide 34: JK flip-flop.

## Slide 35: JK Flip-Flops
Characteristic equation
  Q(t+1) = JQ’(t) + K’Q(t)
J
Q
C
K
J | K | Q(t+1) | next state
0 | 0 | Q(t) | no change
0 | 1 | 0 | Reset
1 | 0 | 1 | Set
1 | 1 | Q’(t) | Complement
Characteristic Table

## Slide 36: T (Toggle) Flip-Flop
Complementing flip-flop
T
Q
C
T | Q(t+1) | next state
0 | Q(t) | no change
1 | Q’(t) | Complement
Characteristic Table
Characteristic equation
  Q(t+1) =
J
Q
C
K
T
D
Q
C
T

## Slide 37: Table 5.1 Flip-Flop Characteristic Tables.