## Slide 1
Al-Azhar University
Faculty of Engineering
Systems and Computer Engineering Dept.
Intelligent Systems Engineering Program
Prof. Ahmed Youssef
ENG 142
Digital and Logic Design (2)

## Slide 2: Synchronous Sequential Logic Part 2

## Slide 3: Table 5.1: Flip-Flop Characteristic Tables.
Characteristic equation
  Q(t+1) = JQ’(t) + K’Q(t)
Characteristic equation
  Q(t+1) = D
Characteristic equation
  Q(t+1) = TQ’(t) + T’Q(t)
    Q(t+1) =Q(t)  T

## Slide 4: Excitation table

## Slide 5: Excitation table (D f/f)
Q(t) | Q(t+1) | D
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1

## Slide 6: Excitation table (SR f/f)
S | R | Q(t+1) | 
0 | 0 | Q(t) | No change
0 | 1 | 0 | Reset
1 | 0 | 1 | Set
1 | 1 | ? | Undefined
Q(t) | Q(t+1) | S | R | 
0 | 0 |  |  | 
0 | 1 |  |  | 
1 | 0 |  |  | 
1 | 1 |  |  | 

## Slide 7: Excitation table (SR f/f)
S | R | Q(t+1) | 
0 | 0 | Q(t) | No change
0 | 1 | 0 | Reset
1 | 0 | 1 | Set
1 | 1 | ? | Undefined
Q(t) | Q(t+1) | S | R | 
0 | 0 | 0 | x | NC, Reset
0 | 1 | 1 | 0 | Set
1 | 0 | 0 | 1 | Reset
1 | 1 | x | 0 | NC, Set

## Slide 8: Excitation table (JK f/f)
Q(t) | Q(t+1) | J | k | 
0 | 0 |  |  | 
0 | 1 |  |  | 
1 | 0 |  |  | 
1 | 1 |  |  | 

## Slide 9: Excitation table (JK f/f)
Q(t) | Q(t+1) | J | k | 
0 | 0 | 0 | x | NC, Reset
0 | 1 | 1 | x | Set, Complement
1 | 0 | x | 1 | Reset, Complement
1 | 1 | x | 0 | NC, Set

## Slide 10: Excitation table (T f/f)
Q(t) | Q(t+1) | T | 
0 | 0 | 0 | NC
0 | 1 | 1 | C
1 | 0 | 1 | C
1 | 1 | 0 | NC

## Slide 11: JK Flip Flop using D Flip Flop
J | K | Q(t) | Q(t+1) | D
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0

## Slide 12: JK flip-flop.

## Slide 13: T Flip Flop using JK Flip Flop
T | Q(t) | Q(t+1) | J | K
0 | 0 | 0 | 0 | x
0 | 1 | 1 | x | 0
1 | 0 | 1 | 1 | x
1 | 1 | 0 | x | 1
J = K = T
J
Q
C
K
T

## Slide 14: T Flip Flop using D Flip Flop
T | Q(t) | Q(t+1) | D
0 | 0 | 0 | 
0 | 1 | 1 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
D
Q
C
T

## Slide 15: Flip-flop Behavior Example
Use the characteristic tables to find the output waveforms for the flip-flop shown:
Clock
D
QD
D
C

## Slide 16: Flip-flop Behavior Example
Use the characteristic tables to find the output waveforms for the flip-flops shown:
T
C
Clock
T

## Slide 17: Flip-Flop Behavior Example
Use the characteristic tables to find the output waveforms for the flip-flop shown:
J
C
K
Clock
J
QJK
K

## Slide 18: Complete the timing diagram assuming you are using a negative- edge triggered JK flip flop.